RUMPISTOL ENSEMBLE (4 PERS) - TECH RIDER

BACKLINE:

1 opretstående piano eller flygel – skal være stemt for nyligt!

1 klaver bænk

1 stole uden ryglæn til harpenist

9 D.I. Boxes (mono)

4 monitor kasser – markeret I sort på tegningen.

KANAL PLAN:

|  | Instrument / channel | Type: | FX: |
| --- | --- | --- | --- |
| 1 | Jens Piano L | Mic | reverb |
| 2 | Jens Piano R | Mic | reverb |
| 3 | Jens Nord Electro L | DI |  |
| 4 | Jens Nord Electro R | DI |  |
| 5 | Jens Octatrack L (backtrack + moog) | DI |  |
| 6 | Jens Octatrack R (backtrack) | DI |  |
| 7 | Jens Moog + 303 | DI |  |
| 8 | Jens Vocal | Mic | reverb |
| 9 | Søren Violin mono DI | DI |  |
| 10 | Søren Violin Mic (DPA 4099) – Phantom | Mic |  |
| 11 | Søren Vocal | DI | reverb |
| 12 | Helene Harp Clean – XLR, Phantom | Mic |  |
| 13 | Helene Harp FX 1 | DI |  |
| 14 | Helene Harp FX 2 - L | DI |  |
| 15 | Helene Harp FX 2 - R | DI |  |
| 16 | Helene Vocal | Mic | reverb |
| 17 | Emil Drums Kick drum | Mic |  |
| 18 | Emil Drums Snare drum | Mic |  |
| 19 | Emil Drums OH | Mic |  |
| 20 | Emil Drums OH | Mic |  |
| 21 | Emil Glockenspiel OH | Mic | reverb |

Opstilling: (publikum er på denne side af stregen)

Drums (Emil)             Piano + Synths (Jens)

Violin (Maria)         Harp (Helene)

Lys:

Pin spot på hver enkelt musiker helst lige fra oven. Ellers så mørkt som muligt.

Røg maskine og stroboskob på udvalgte tidspunkter er meget velkomne!

Pausemusik:

Brug venligst Spotify Playlisten “Rumpistol Vinterjazz 2023” før og efter koncert.

https://open.spotify.com/playlist/6LfFM8lSFMwUCatwoiFP7h?si=8fc423963d304677

Telefonnummer til artist ved spørgsmål til rider: 60668657

I TILFÆLDE AF YDERLIGERE BACKLINE (KUN EFTER SÆRLIG AFTALE):

1 Drum kit (for Emil)

One 20-22” bass drum (not power depth) preferably with coated Remo ambassador head

One 14-16” floortom on legs (not rack mount) preferably w. coated Remo Ambassador

One 12-13” tomtom (not power depth) preferably w. coated Remo Ambassador

One 14” x 5” snaredrum w. coated Remo Ambassador

All of a good brand. Preferably Ludwig, but DW, Sonor, Tama, Premier or likes are okay. Preferably not Pearl.

20 inch thin ride cymbal of a good brand

One snaredrum stand

3 cymbal stands

One drum throne/stool

One hihat stand and two bassdrum pedals (preferably DW or Premier)

Rug for the kit

Small and low table/chair/flightcase for Emil´s electronics